## Slide 1: About the Presentations
The presentations cover the objectives found in the opening of each chapter.
All chapter objectives are listed in the beginning of each presentation.
You may customize the presentations to fit your class needs.
Some figures from the chapters are included. A complete set of images from the book can be found on the Instructor Companion site.
Notes: About the Presentations
The presentations cover the objectives found in the opening of each chapter.
All chapter objectives are listed in the beginning of each presentation.
You may customize the presentations to fit your class needs.
Some figures from the chapters are included. A complete set of images from the book can be found on the Instructor Resources disc.

## Slide 2: A+ Guide to Hardware, 9th Edition
Chapter 1
First Look at Computer Parts and Tools
Notes: A+ Guide to Hardware, 9th Edition
Chapter 1
First Look at Computer Parts and Tools

## Slide 3: Objectives
Identify the various parts inside a desktop computer case and describe how they connect together and are compatible
Identify the various ports, slots, and internal components of a laptop computer and explain special concerns when supporting and maintaining laptops
Notes: Objectives
Identify the various parts inside a desktop computer case and describe how they connect together and are compatible
Identify the various ports, slots, and internal components of a laptop computer and explain special concerns when supporting and maintaining laptops

## Slide 4: Objectives
Describe various hardware components in mobile devices and types of wired and wireless connections mobile devices can make
Describe the purpose of various tools you will need as a computer hardware technician
Notes: Objectives
Describe various hardware components in mobile devices and types of wired and wireless connections mobile devices can make
Describe the purpose of various tools you will need as a computer hardware technician

## Slide 5: What’s Inside the Case
Computer Case
  Sometimes called “chassis”
  Holds
    Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    Tower case – sits upright and can hold several drives
    Desktop case – lies flat and sometimes holds monitor
    Mobile case – used with laptops and tablets
    All-in-one case – used with all-in-one computer
Notes: What’s Inside the Case
Computer Case
  Sometimes called “chassis”
  Holds
    Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    Tower case – sits upright and can hold several drives
    Desktop case – lies flat and sometimes holds monitor
    Mobile case – used with laptops and tablets
    All-in-one case – used with all-in-one computer

## Slide 6: What’s Inside the Case
Table 1-1 Ports used with desktop and mobile computers
Notes: What’s Inside the Case
Computer Case
  Sometimes called “chassis”
  Holds
    Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    Tower case – sits upright and can hold several drives
    Desktop case – lies flat and sometimes holds monitor
    Mobile case – used with laptops and tablets
    All-in-one case – used with all-in-one computer

## Slide 7: What’s Inside the Case
Table 1-1 Ports used with desktop and mobile computers (continued)
Notes: What’s Inside the Case
Computer Case
  Sometimes called “chassis”
  Holds
    Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    Tower case – sits upright and can hold several drives
    Desktop case – lies flat and sometimes holds monitor
    Mobile case – used with laptops and tablets
    All-in-one case – used with all-in-one computer

## Slide 8: What’s Inside the Case
Table 1-1 Ports used with desktop and mobile computers (continued)
Notes: What’s Inside the Case
Computer Case
  Sometimes called “chassis”
  Holds
    Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    Tower case – sits upright and can hold several drives
    Desktop case – lies flat and sometimes holds monitor
    Mobile case – used with laptops and tablets
    All-in-one case – used with all-in-one computer

## Slide 9: What’s Inside the Case
Figure 1-2 Inside the computer case
Notes: What’s Inside the Case
Computer Case
  Sometimes called “chassis”
  Holds
    Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    Tower case – sits upright and can hold several drives
    Desktop case – lies flat and sometimes holds monitor
    Mobile case – used with laptops and tablets
    All-in-one case – used with all-in-one computer

## Slide 10: What’s Inside the Case
Motherboard – sometimes called system board
  Largest and most important circuit board
Processor – central processing unit (CPU)
  Processes most of the data and instructions for the entire system
  CPUs generate heat and require a heat sink and fan (together called the processor cooler)
    A heat sink consists of metal fins that draw heat away from a component
Notes: What’s Inside the Case
Motherboard – sometimes called system board
  Largest and most important circuit board
Processor – central processing unit (CPU)
  Processes most of the data and instructions for the entire system
  CPUs generate heat and require a heat sink and fan (together called the processor cooler)
    A heat sink consists of metal fins that draw heat away from a component

## Slide 11: What’s Inside the Case
Expansion cards - also called adapter cards
  A circuit board that provides more ports than those provided by the motherboard
  Today, most ports are provided by motherboards
Figure 1-4 Ports provided by the motherboard
Notes: What’s Inside the Case
Expansion cards - also called adapter cards
  A circuit board that provides more ports than those provided by the motherboard
  Today, most ports are provided by motherboards

## Slide 12: What’s Inside the Case
Memory modules – random access memory (RAM)
  Temporary storage for data and instructions as they are being processed by the CPU
  Dual inline memory module (DIMM) slots hold memory modules
Figure 1-6 A DIMM holds RAM and is mounted directly on a motherboard
Notes: What’s Inside the Case
Memory modules – random access memory (RAM)
  Temporary storage for data and instructions as they are being processed by the CPU
  Dual inline memory module (DIMM) slots hold memory modules

## Slide 13: What’s Inside the Case
Hard drives and other drives
  Hard drives may also be called hard disk drive (HDD)
    Permanent storage used to hold data and programs
  Other drives include: optical drive and tape drive
Figure 1-7 Two types of hard drives (larger magnetic drive and smaller solid-state drive) and a DVD drive
Notes: What’s Inside the Case
Hard drives and other drives
  Hard drives may also be called hard disk drive (HDD)
    Permanent storage used to hold data and programs
  Other drives include: optical drive and tape drive

## Slide 14: What’s Inside the Case
Power supply – also called power supply unit (PSU)
  Receives and converts house current so that components inside the case can use it
  Most come with a dual-voltage selector switch
    Allows switching input voltage from 115V to 220V
Notes: What’s Inside the Case
Power supply – also called power supply unit (PSU)
  Receives and converts house current so that components inside the case can use it
  Most come with a dual-voltage selector switch
    Allows switching input voltage from 115V to 220V

## Slide 15: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Form factors: standards that describe the size, shape, screw hole positions, and major features of computer cases, power supplies, and motherboards
  Necessary so that all will be compatible with each other
Two form factors used by most desktop and tower computer cases and power supplies:
  ATX
  Micro-ATX
Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Form factors: standards that describe the size, shape, screw hole positions, and major features of computer cases, power supplies, and motherboards
  Necessary so that all will be compatible with each other
Two form factors used by most desktop and tower computer cases and power supplies:
  ATX
  Micro-ATX

## Slide 16: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
ATX (Advanced Technology Extended)
  Most commonly used form factor today
  Originally developed by Intel in 1995
  It is an open, nonproprietary industry specification
An ATX power supply has a variety of power connectors
  Power connectors have evolved because new technologies require more power
  Common ATX power connectors are listed on the following slides
Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
ATX (Advanced Technology Extended)
  Most commonly used form factor today
  Originally developed by Intel in 1995
  It is an open, nonproprietary industry specification
An ATX power supply has a variety of power connectors
  Power connectors have evolved because new technologies require more power
  Common ATX power connectors are listed on the following slides

## Slide 17: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
20-pin P1 connector: used by the first ATX power supplies and motherboards
4-pin and 8-pin auxiliary connectors: used to provide and additional 12 V of power for evolving CPUs
24-pin or 20+4-pin P1 connector: the older 20-pin P1 connector still worked in this connector
  Supported the new PCI Express slots
6-pin and 8-pin PCIe connectors: connect directly to the video card
  Video cards draw the most power in a system
Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
20-pin P1 connector: used by the first ATX power supplies and motherboards
4-pin and 8-pin auxiliary connectors: used to provide and additional 12 V of power for evolving CPUs
24-pin or 20+4-pin P1 connector: the older 20-pin P1 connector still worked in this connector
  Supported the new PCI Express slots
6-pin and 8-pin PCIe connectors: connect directly to the video card
  Video cards draw the most power in a system

## Slide 18: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Micro-ATX form factor
  Major variation of ATX
  Reduces total cost of a system by:
    Reducing number of expansion slots on motherboard
    Reducing power supplied to the board
    Allowing for a smaller case size
  Uses a 24-pin P1 connector
    Not likely to have as many extra wires and connectors as those on the ATX power supply
Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Micro-ATX form factor
  Major variation of ATX
  Reduces total cost of a system by:
    Reducing number of expansion slots on motherboard
    Reducing power supplied to the board
    Allowing for a smaller case size
  Uses a 24-pin P1 connector
    Not likely to have as many extra wires and connectors as those on the ATX power supply

## Slide 19: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Figure 1-17 This microATX motherboard by Biostar is designed to support an AMD processor
Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Micro-ATX form factor
  Major variation of ATX
  Reduces total cost of a system by:
    Reducing number of expansion slots on motherboard
    Reducing power supplied to the board
    Allowing for a smaller case size
  Uses a 24-pin P1 connector
    Not likely to have as many extra wires and connectors as those on the ATX power supply

## Slide 20: Drives, Their Cables, and Connectors
Hard Drives
  Two standards:
    Serial ATA standard (SATA)
      Used by most drives today
      Get power from a power cable that connects to the drive using a SATA power connector
    Parallel ATA (PATA) – slower than SATA
      Also called IDE interface
      Used 40-pin ribbon cable and connector
      Two connectors on a motherboard for two data cables
      Found in most older desktop computers
Notes: Drives, Their Cables, and Connectors
Hard Drives
  Two standards:
    Serial ATA standard (SATA)
      Used by most drives today
      Get power from a power cable that connects to the drive using a SATA power connector
    Parallel ATA (PATA) – slower than SATA
      Also called IDE interface
      Used 40-pin ribbon cable and connector
      Two connectors on a motherboard for two data cables
      Found in most older desktop computers

## Slide 21: First Look at Laptop Computers
Laptop (notebook): portable computer
  Variation of a laptop is a netbook
    Smaller and has less features than laptop
Comparing laptops to desktop computers
  Use the same technology as desktops
  Smaller, portable, and use less power
  Replacement parts cost more than desktops
Laptops offer a variety of ports and slots
Notes: First Look at Laptop Computers
Laptop (notebook): portable computer
  Variation of a laptop is a netbook
    Smaller and has less features than laptop
Comparing laptops to desktop computers
  Use the same technology as desktops
  Smaller, portable, and use less power
  Replacement parts cost more than desktops
Laptops offer a variety of ports and slots

## Slide 22: First Look at Laptop Computers
Figure 1-23 Ports and slots on a laptop computer
Notes: First Look at Laptop Computers

## Slide 23: First Look at Laptop Computers
Ports common to laptops include:
  USB, FireWire, network, dial-up modem, audio, and video ports
Most laptops include slots for flash memory cards
When a laptop is missing a port or slot, you can use a USB dongle to provide the port or slot
  Examples:
    USB to RJ-45 dongle to connect to a wired network
    USB to Wi-Fi dongle to connect to a wireless network
Notes: First Look at Laptop Computers
Ports common to laptops include:
  USB, FireWire, network, dial-up modem, audio, and video ports
Most laptops include slots for flash memory cards
When a laptop is missing a port or slot, you can use a USB dongle to provide the port or slot
  Examples:
    USB to RJ-45 dongle to connect to a wired network
    USB to Wi-Fi dongle to connect to a wireless network

## Slide 24: First Look at Laptop Computers
Figure 1-25 USB to RJ-45 dongle provides a network port to connect to a wired network
Figure 1-26 This USB to Wi-Fi adapter plugs into a USB port to connect to a local wireless network
Notes: First Look at Laptop Computers

## Slide 25: Special Keys, Buttons, and Input Devices on a Laptop
Button or switches might be above the keyboard
  Most of the same settings that these buttons control may also be changed using Windows tools
  Some settings might be:
    Volume
    Keyboard backlight
    Touch pad on or off
    Screen brightness and screen orientation
    Dual displays
    Bluetooth or Wi-Fi
    Media options
    GPS on or off
Notes: Special Keys, Buttons, and Input Devices on a Laptop
Button or switches might be above the keyboard
  Most of the same settings that these buttons control may also be changed using Windows tools
  Some settings might be:
    Volume
    Keyboard backlight
    Touch pad on or off
    Screen brightness and screen orientation
    Dual displays
    Bluetooth or Wi-Fi
    Media options
    GPS on or off

## Slide 26: ExpressCard Slots
Most peripheral devices on today’s laptops use a USB port to connect to a laptop
Before USB, laptops offered ExpressCard slots
  Sometimes called PCMCIA cards
ExpressCard matches PCI Express and USB 2.0
  Two sizes: ExpressCard/34 and ExpressCard/54
  Not backward compatible
  Hot-pluggable, hot-swappable, and supports autoconfiguration
Notes: ExpressCard Slots
Most peripheral devices on today’s laptops use a USB port to connect to a laptop
Before USB, laptops offered ExpressCard slots
  Sometimes called PCMCIA cards
ExpressCard matches PCI Express and USB 2.0
  Two sizes: ExpressCard/34 and ExpressCard/54
  Not backward compatible
  Hot-pluggable, hot-swappable, and supports autoconfiguration

## Slide 27: ExpressCard Slots
Windows services for ExpressCard
  Socket service establishes communication between the card and the laptop
  Card service provides the device driver to interface with the card after the socket is created
Removing card from ExpressCard slot
  Use the Safely Remove Hardware icon in the notification area to stop one card before inserting another
  Proceed to eject the card
Notes: ExpressCard Slots
Windows services for ExpressCard
  Socket service establishes communication between the card and the laptop
  Card service provides the device driver to interface with the card after the socket is created
Removing card from ExpressCard slot
  Use the Safely Remove Hardware icon in the notification area to stop one card before inserting another
  Proceed to eject the card

## Slide 28: Docking Stations
Some laptops have a connector called a docking port
A docking station provides ports to allow a laptop to easily connect to a full-sized monitor, keyboard, AC power adapter, and other peripheral devices
To use a docking station:
  Plug all peripherals into docking station
  Connect laptop to the station
  No software needed
Notes: Docking Stations
Some laptops have a connector called a docking port
A docking station provides ports to allow a laptop to easily connect to a full-sized monitor, keyboard, AC power adapter, and other peripheral devices
To use a docking station:
  Plug all peripherals into docking station
  Connect laptop to the station
  No software needed

## Slide 29: Laptop Internal Components
Figure 1-36 Bottom of a laptop with cover removed
Notes: Laptop Internal Components

## Slide 30: Laptop Internal Components
List of important components:
  Battery pack
  Hard drive
  CPU, heat sink, and fan
  Memory
  Wireless card
  System board
  Optical drive
Notes: Laptop Internal Components
List of important components:
  Battery pack
  Hard drive
  CPU, heat sink, and fan
  Memory
  Wireless card
  System board
  Optical drive

## Slide 31: What’s Inside an All-in-One Computer
All-in-one computer: uses a mix of components sized for a desktop and a laptop
  For some components, you’ll need to buy replacements from the manufacturer because they are most likely proprietary
  See the service manual for specific directions about replacing parts
Notes: What’s Inside an All-in-One Computer
All-in-one computer: uses a mix of components sized for a desktop and a laptop
  For some components, you’ll need to buy replacements from the manufacturer because they are most likely proprietary
  See the service manual for specific directions about replacing parts

## Slide 32: What’s Inside an All-in-One Computer
Figure 1-38 Components inside an all-in-one computer
Notes: What’s Inside an All-in-One Computer

## Slide 33: Maintaining Laptops and Mobile Devices
General guidelines:
  Do not touch LCD panel with sharp objects
  Do not pick up or hold by the lid
  Use OEM recommended battery packs
  Do not tightly pack in a suitcase – use carrying case
  Do not move while hard drive is being accessed
  Do not put close to appliances generating strong magnetic field
  Always use passwords to protect your laptop when connected to a public network or if device is stolen
Notes: Maintaining Laptops and Mobile Devices
General guidelines:
  Do not touch LCD panel with sharp objects
  Do not pick up or hold by the lid
  Use OEM recommended battery packs
  Do not tightly pack in a suitcase – use carrying case
  Do not move while hard drive is being accessed
  Do not put close to appliances generating strong magnetic field
  Always use passwords to protect your laptop when connected to a public network or if device is stolen

## Slide 34: Maintaining Laptops and Mobile Devices
General guidelines (cont’d):
  Keep notebook at room temperature
  Keep away from smoke, water, dust
  Do not power up and down unnecessarily
  Do not run it while it is in the case, resting on pillow or covered by a blanket
  Protect notebook against ESD
  Remove CD/DVD or USB flash drives before traveling
  Take precautions if notebook gets wet
  Keep current backups of important data
Notes: Maintaining Laptops and Mobile Devices
General guidelines (cont’d):
  Keep notebook at room temperature
  Keep away from smoke, water, dust
  Do not power up and down unnecessarily
  Do not run it while it is in the case, resting on pillow or covered by a blanket
  Protect notebook against ESD
  Remove CD/DVD or USB flash drives before traveling
  Take precautions if notebook gets wet
  Keep current backups of important data

## Slide 35: Maintaining Laptops and Mobile Devices
Cleaning tips:
  Clean LCD panel with a soft dry cloth
  Use compressed air
    To clean keyboard, track ball, and touch pad
    To blow out air vents
    Remove keyboard if keys are sticking and then blow air under keys
  Use contact cleaner
    Remove battery and clean battery connections
Notes: Maintaining Laptops and Mobile Devices
Cleaning tips:
  Clean LCD panel with a soft dry cloth
  Use compressed air
    To clean keyboard, track ball, and touch pad
    To blow out air vents
    Remove keyboard if keys are sticking and then blow air under keys
  Use contact cleaner
    Remove battery and clean battery connections

## Slide 36: First Look at Mobile Device Hardware
A smart phone is a cell phone with added capabilities
  Ability to send/receive text messages with photos, video, or other multimedia content
  Web browsing
  Manage email
  Play games
  Take photos and video
  Use a variety of apps
Notes: First Look at Mobile Device Hardware
A smart phone is a cell phone with added capabilities
  Ability to send/receive text messages with photos, video, or other multimedia content
  Web browsing
  Manage email
  Play games
  Take photos and video
  Use a variety of apps

## Slide 37: First Look at Mobile Device Hardware
Tablet is larger than a smart phone with similar functions
Most connect to Wi-Fi and Bluetooth and some have cellular network connectivity
  Some can make phone calls and use MMS
Phablet – same capabilities of a smart phone or tablet
  Smaller than a tablet and larger than a smart phone
Notes: First Look at Mobile Device Hardware
Tablet is larger than a smart phone with similar functions
Most connect to Wi-Fi and Bluetooth and some have cellular network connectivity
  Some can make phone calls and use MMS
Phablet – same capabilities of a smart phone or tablet
  Smaller than a tablet and larger than a smart phone

## Slide 38: First Look at Mobile Device Hardware
Other mobile devices
  E-readers
  Smart cameras
  Wearable technology devices
    Smart watches, wristbands, arm bands, eyeglasses, headsets, and clothing
Notes: First Look at Mobile Device Hardware
Other mobile devices
  E-readers
  Smart cameras
  Wearable technology devices
    Smart watches, wristbands, arm bands, eyeglasses, headsets, and clothing

## Slide 39: Connection Types
Some ways a mobile device connects to outside world:
  Wi-Fi local wireless network and cellular network
  Bluetooth and Infrared
  Near Field Communication (NFC)
  Wired connection
  Tethering and mobile hotspots
Notes: Connection Types
Some ways a mobile device connects to outside world:
  Wi-Fi local wireless network and cellular network
  Bluetooth and Infrared
  Near Field Communication (NFC)
  Wired connection
  Tethering and mobile hotspots

## Slide 40: Connection Types
A mobile device can use the following to sense its position:
  Gyroscope or accelerometer
    Motion and position sensing device
    Helps to adjust screen orientation
    Used by games to sense device movement
  GPS
    Mobile devices might contain a GPS receiver
    Routinely reports its position to the owner of the OS
    Geotracking: possible for companies to track device’s whereabouts
Notes: Connection Types
A mobile device can use the following to sense its position:
  Gyroscope or accelerometer
    Motion and position sensing device
    Helps to adjust screen orientation
    Used by games to sense device movement
  GPS
    Mobile devices might contain a GPS receiver
    Routinely reports its position to the owner of the OS
    Geotracking: possible for companies to track device’s whereabouts

## Slide 41: Storage Devices
Mobile devices store apps and data on a solid state drive (SSD)
  A type of flash memory
A device might have an external slot for a smart card to provide extra storage
Figure 1-49 An Android device might provide a memory card slot to allow for extra storage
Notes: Storage Devices
Mobile devices store apps and data on a solid state drive (SSD)
  A type of flash memory
A device might have an external slot for a smart card to provide extra storage

## Slide 42: Mobile Device Accessories
Examples of accessories:
  Wireless keyboards
  Speakers
  Ear buds
  Headsets
  Game pads
  Docking stations
  Printers
  USB adapters
  Credit card readers
Notes: Mobile Device Accessories
Examples of accessories:
  Wireless keyboards
  Speakers
  Ear buds
  Headsets
  Game pads
  Docking stations
  Printers
  USB adapters
  Credit card readers

## Slide 43: Field-Serviceable Parts for Mobile Devices
There are few FRU in mobile devices
It is possible to replace screens in some mobile devices
  A support technician is not generally expected to do this
SIM cards and batteries can be replaced
Notes: Field-Serviceable Parts for Mobile Devices
There are few FRU in mobile devices
It is possible to replace screens in some mobile devices
  A support technician is not generally expected to do this
SIM cards and batteries can be replaced

## Slide 44: Tools Used By a Computer Hardware Technician
Essential tools
  ESD strap (ground bracelet)
  Flat-head screwdriver
  Phillips-head or cross-head screwdriver
  Torx screwdriver set (size T15)
  Insulated tweezers
  Extractor
  OS recovery CD or DVD
Many other non-essential tools exists
Use a toolbox
Notes: Tools Used By a Computer Hardware Technician
Essential tools
  ESD strap (ground bracelet)
  Flat-head screwdriver
  Phillips-head or cross-head screwdriver
  Torx screwdriver set (size T15)
  Insulated tweezers
  Extractor
  OS recovery CD or DVD
Many other non-essential tools exists
Use a toolbox

## Slide 45: Tools Used By a Computer Hardware Technician
Figure 1-52 Tools used by IT support technicians when maintaining, repairing, or upgrading computers
Notes: Tools Used By a Computer Hardware Technician
Essential tools
  ESD strap (ground bracelet)
  Flat-head screwdriver
  Phillips-head or cross-head screwdriver
  Torx screwdriver set (size T15)
  Insulated tweezers
  Extractor
  OS recovery CD or DVD
Many other non-essential tools exists
Use a toolbox

## Slide 46: Post Diagnostic Cards
Post Diagnostic Cards
  Helps discover, report computer errors and conflicts at power-on self test (POST)
    Tests performed by startup UEFI/BIOS
Figure 1-56 Post Code Master diagnostic card by Microsystems Developments, Inc. installs in a PCI slot
Notes: Post Diagnostic Cards
Post Diagnostic Cards
  Helps discover, report computer errors and conflicts at power-on self test (POST)
    Tests performed by startup UEFI/BIOS

## Slide 47: Post Diagnostic Cards
Firmware – programs and data stored on the motherboard
Two types of firmware may be used:
  BIOS (basic input/output system) contains:
    System BIOS
    Startup BIOS
    BIOS setup
  UEFI (Unified Extensible Firmware Interface)
    More robust and secure than BIOS
    Can assure boot is secure and no rogue OS hijacks the system
Notes: Post Diagnostic Cards
Firmware – programs and data stored on the motherboard
Two types of firmware may be used:
  BIOS (basic input/output system) contains:
    System BIOS
    Startup BIOS
    BIOS setup
  UEFI (Unified Extensible Firmware Interface)
    More robust and secure than BIOS
    Can assure boot is secure and no rogue OS hijacks the system

## Slide 48: Power Supply Tester
Power Supply Tester
  Measures output of each power supply connector
Figure 1-57 Use a power supply tester to test the output of each power connector on a power supply
Notes: Power Supply Tester
Power Supply Tester
  Measures output of each power supply connector

## Slide 49: Multimeter
Multimeter
  Measures several characteristics of electricity in a variety of devices
Figure 1-58 This digital multimeter can be set to measure voltage, resistance, or continuity
Notes: Multimeter
Multimeter
  Measures several characteristics of electricity in a variety of devices

## Slide 50: Loopback Plugs
Loopback plug
  Used to test a port in a computer or other device to make sure the port is working
    May also test the throughput or speed of port
Figure 1-59 A loopback plug testing a network port and network cable
Notes: Loopback Plugs
Loopback plug
  Used to test a port in a computer or other device to make sure the port is working
    May also test the throughput or speed of port

## Slide 51: Summary
Ports on a computer might include video, RJ-45, audio, S/PDIF, USB, FireWire, eSATA, and PS/2
Internal computer components include the motherboard, processor, expansion cards, DIMM modules, hard drive, optical drive, tape drive, and power supply
Form factors used by cases, power supplies, and motherboards are ATX and micro-ATX
Power connectors include the 20-pin P1, 24-pin P1, 4-pin and 8-pin auxiliary motherboard, 4-pin Molex, 15-pin SATA, 4-pin Berg, and 6/8-pin PCIe
Notes: Summary
Ports on a computer might include video, RJ-45, audio, S/PDIF, USB, FireWire, eSATA, and PS/2
Internal computer components include the motherboard, processor, expansion cards, DIMM modules, hard drive, optical drive, tape drive, and power supply
Form factors used by cases, power supplies, and motherboards are ATX and micro-ATX
Power connectors include the 20-pin P1, 24-pin P1, 4-pin and 8-pin auxiliary motherboard, 4-pin Molex, 15-pin SATA, 4-pin Berg, and 6/8-pin PCIe

## Slide 52: Summary
Most hard drives, optical drives, and tape drives use the serial ATA (SATA) standards
Laptop computers use function keys to control many features of the laptop
A laptop may have an ExpressCard/34 or ExpressCard/54 slot for expansion
Internal laptop components include keyboard, hard drive, memory, smart card reader, optical drive, wireless card, screen, DC jack, battery pack, touch pad, speaker, system board, and CPU, heat sink/fan
Notes: Summary
Most hard drives, optical drives, and tape drives use the serial ATA (SATA) standards
Laptop computers use function keys to control many features of the laptop
A laptop may have an ExpressCard/34 or ExpressCard/54 slot for expansion
Internal laptop components include keyboard, hard drive, memory, smart card reader, optical drive, wireless card, screen, DC jack, battery pack, touch pad, speaker, system board, and CPU, heat sink/fan

## Slide 53: Summary
An all-in-one computer uses a combination of components designed for desktop computers and laptops
Mobile devices an IT support technician may service include smart phones, tablets, phablets, e-readers, smart cameras, GPS devices, and wearable technology devices
A mobile device might make a connection using a cellular network, Wi-Fi network, Bluetooth, IR, NFC, tethering, creating its own hotspot, or a wired connection
Notes: Summary
An all-in-one computer uses a combination of components designed for desktop computers and laptops
Mobile devices an IT support technician may service include smart phones, tablets, phablets, e-readers, smart cameras, GPS devices, and wearable technology devices
A mobile device might make a connection using a cellular network, Wi-Fi network, Bluetooth, IR, NFC, tethering, creating its own hotspot, or a wired connection

## Slide 54: Summary
Common tools for a computer hardware technician include an ESD strap, screwdrivers, tweezers, flashlight, compressed air, and cleaning solutions and pads
Special tools a PC support technician might need include a POST diagnostic card, power supply tester, multimeter, and loopback plugs
Notes: Summary
Common tools for a computer hardware technician include an ESD strap, screwdrivers, tweezers, flashlight, compressed air, and cleaning solutions and pads
Special tools a PC support technician might need include a POST diagnostic card, power supply tester, multimeter, and loopback plugs